Updated:  5-22-2019 BEM

Most turnouts on the layout will be by manual operation in order to provide more operator interaction during an operating session.

- Crossover and Wye configurations shall be automated to minimize derailments

- Hard to reach turnouts will be automated to prevent inadvertent damage to scenery and equipment

The following practices apply to the GMRC layout.

Turnout Control:

- Ground Throws:

  - A Caboose Industries 218S ground throw is the recommended model for turnouts with non-powered frogs.

    - the 218S ground throw comes with selectable end connectors

    - for Peco turnouts, use the connector with the ‘hole’ that fits over the pin on the turnout’s throw-bar

    - for Shinohara turnouts, use the connector with the ‘pin’ that fits into the hole in the turnout throw-bar

  - A Caboose Industries 220S ground throw with SPDT switch contacts is the recommended model for turnouts…

    - with frogs that can be powered

    - where power is routed to a section of track

    - the 220S ground throw comes with selectable end connectors

    - select the end connector that fits the brand of turnout

- Installing the ground throw:

  - To prevent the throw handle from going all the way to the base, the anchoring track nails will go through a 4 mm ‘spacer’ bead

  - Occasionally it is necessary to put a bead of ‘Fix-All’ adhesive on the bottom of the ground throw to keep it fastened in place

- Automated Turnout Motors:

  - Use the pre-assembled Tortoise units

    - the telco jack is for use with the fascia control panels

    - the 3-pin euro-connector is for use with SPDT control switches such as on a 220S ground throw

  - The pre-assembled Hankscraft motor units with the micro-switches and telco jack are to be phased out

    - The plastic paddle ‘swing-arm’ on these units frequently crack causing the motor to continuously spin.   They should be replaced with Tortoises rather than repaired.

- Turnout Control Boxes:

  - Custom ‘Control Boxes’ with toggle switches, diagram, indicator lights and telco jacks are used to control automated turnouts

  - A custom made length of 6-conductor telco cable is used to connect the turnout panel to the turnout motor

    - see ‘GMRC – Turnout Control Boxes’ for design and construction of these units

- continued on page 2     -

- Hybrid Crossover Control

  - Crossovers can be controlled using one 220S ground throw and one Tortoise motor with the euro connector

  - The front turnout is manually controlled by the 220S ground throw

  - The back turnout is electrically controlled by a Tortoise motor.

    - See ‘GMRC – Turnout Control – SPDT Switch’ for design and wiring of this practice